## Slide 1
Start
Configure direction of Atmega32 pins (inputs – outputs)
Initialize LCD, ADC, SPI, TC72, RTC, Keypad, Timer Interrupt, UART
While
(True)
Get time (RTC)
Check daytime/nighttime (LDR)
Disable INT2,
Deactivate IR sensor (not count people)
Reset people counter
Enable INT2 (Turn on LED for each visitor),
Activate IR sensor (count people)
Increment people counter
Day
Night
Activate
Water pump
Check timer-pumping mode (using input from Keypad)
Time up
Time not up
Monitor Temperature and Moisture
(compare with thresholds input from UART terminal)
Activate Pumping
(Water or mist maker or both)
Lower than threshold
>= threshold
If people-monitoring button pressed
LCD display people monitor screen
If main-screen button pressed
LCD Display main screen
If status - setup button pressed
LCD display setting up temperature & moisture screen
Get data from UART connect
If status - setup button pressed
LCD display timer-pump setup screen
Get data from keypad
True
True
True
True
False
False
False
False